Arduino Workshop
Special Interest Group Robotics -
eHacks
Getting Started with Arduino and the Arduino IDE

---
What is Arduino?
- Arduino is an open source hardware platform
- Simple and easy to use
- Cheaper than some other platforms

---
Arduino Boards

---
The Hardware
This workshop will focus on the Arduino UNO R3 microcontroller
- 8 bit Atmega 328P microcontroller
- 16 Mhz clock, 32 KB flash memory, 2 KB ram, 1 KB of EEPROM
- 5V
- 14 digital I/O (6 PWM), 6 analog input
- $25

---
The Software
- Arduino IDE v 1.6.7
- Opensource IDE written in Java available on Windows, Mac, Linux, BSD and more
- Verify, compile, upload, library management, serial plotter, and serial monitor

---
Getting Started
- Download the IDE from https://www.arduino.cc/en/Main/Software
- Install any required drivers if using cheap Arduino knockoffs – Windows and Mac only
- Connect to your Arduino UNO using a printer cable
- Start the IDE
- Select the proper Arduino model from Tools→Board
- Select the proper port from Tools->Port

---
Parts of an Arduino Program
- Setup – function is run once at startup
- Should be used to set outputs, connect to serial, initilization
- Loop – runs repeatedly after setup until the Arduino looses power
- Procerdural code goes here
Arduino uses a C based language, though there is no main function.
The IDE loads generic Arduino libraries for you, no need to include them.

---
Hello World
In the world of microcontrollers, blinking an LED is considered a Hello World
Hardware Setup:

---
Hello World
Program
void setup()
{
  // Set Pin 7 to output
  pinMode(7, OUTPUT);
}
void loop()
{
  // Write a HIGH signal to Pin 7 turing the LED on
  digitalWrite(7, HIGH);
  // delay is in miliseconds
  delay(1000);
  // Write a LOW signal to Pin 7 turning the LED off
  digitalWrite(7, LOW);
  delay(1000);
}