Arduino Workshop
Special Interest Group Robotics -
eHacks
Getting Started with Arduino and the Arduino IDE

---
What is Arduino?
- Arduino is an open source hardware platform
- Simple and easy to use
- Cheaper than some other platforms

---
Arduino Boards

---
The Hardware
This workshop will focus on the Arduino UNO R3 microcontroller
- 8 bit Atmega 328P microcontroller
- 16 Mhz clock, 32 KB flash memory, 2 KB ram, 1 KB of EEPROM
- 5V
- 14 digital I/O (6 PWM), 6 analog input
- $25

---
The Software
- Arduino IDE v 1.6.7
- Opensource IDE written in Java available on Windows, Mac, Linux, BSD and more
- Verify, compile, upload, library management, serial plotter, and serial monitor

---
Getting Started
- Download the IDE from https://www.arduino.cc/en/Main/Software
- Install any required drivers if using cheap Arduino knockoffs – Windows and Mac only
- Connect to your Arduino UNO using a printer cable
- Start the IDE
- Select the proper Arduino model from Tools→Board
- Select the proper port from Tools->Port

---
Parts of an Arduino Program
- Setup – function is run once at startup
- Should be used to set outputs, connect to serial, initilization
- Loop – runs repeatedly after setup until the Arduino looses power
- Procerdural code goes here
Arduino uses a C based language, though there is no main function.
The IDE loads generic Arduino libraries for you, no need to include them.

---
Hello World
In the world of microcontrollers, blinking an LED is considered a Hello World
Hardware Setup:

---
Hello World
Program
void setup()
{
  // Set Pin 7 to output
  pinMode(7, OUTPUT);
}
void loop()
{
  // Write a HIGH signal to Pin 7 turing the LED on
  digitalWrite(7, HIGH);
  // delay is in miliseconds
  delay(1000);
  // Write a LOW signal to Pin 7 turning the LED off
  digitalWrite(7, LOW);
  delay(1000);
}

---
Debugging your code
- It is not possible to print debugging information to the screen as an Arduino has no screen
- We use Serial to see debugging information
- Another option is to use an LCD display connected to the Arduino

---
Serial Communication
- Use the RX and TX ports on the Arduino or the printer cable connection to your computer
- Steps:
  - Initialize the connection using a baudrate
    - We will be using 9600 as the baudrate
  - Wait for the connection to be established
  - Send data or Receive data from serial
  - Read data from Serial Monitor in Arduino IDE

---
Hello World with Serial
void setup()
{
  // Set Pin 7 to output
  pinMode(7, OUTPUT);
  Serial.begin(9600);
}
void loop()
{
  // Write a HIGH signal to Pin 7 turing the LED on
  digitalWrite(7, HIGH);
  // delay is in miliseconds
  Serial.write(„LED is ON“); // write to serial port
  delay(1000);
  // Write a LOW signal to Pin 7 turning the LED off
  digitalWrite(7, LOW);
  Serial.write(„LED is OFF“); // write to serial port
  delay(1000);
}
Program
A few caveates:
 You may want to wait for the serial connection by adding a while loop after the initial serial connection:
while(!Serial) {;}
Checking if the serial connection is still available can and should also be done: Serial.available()
Now open the Arduino IDE‘s Serial Monitor (Tools→Serial Monitor) and watch the results

---
Reading from Serial
A Serial connection can also be used to send commands to an Arduino
void loop() // Setup is the same as before
{
    char command = 0; //char to hold command byte
    //if a byte is waiting in the serial buffer
    if (Serial.available() > 0)
    {
      command = Serial.read(); //read the byte and store it.
    }
    switch(command)
    {
       case ‚H‘:
       digitalWrite(7, HIGH); // Turn on LED
       break;
       case ‚L‘:
       digitalWrite(7, LOW); // Turn off LED
      break;
    }
}
You may wish to flush the buffer at the end of loop:
Serial.flush();
To test, open the Serial Monitor and try sending H and L

---
Reading the state of a PIN
- Besides using PINs as output, they can also be used as input.
- We will use a push button to turn on the LED

---
Reading the state of a PIN
void setup()
{
  // setup pins as input or output
 pinMode(7, OUTPUT);
 pinMode(2, INPUT);
}
void loop()
{
  // read the state of the button
 if(digitalRead(2) == HIGH)
  { // turn on the LED since the button is pressed
    digitalWrite(7, HIGH);
  }else
  { // turn off the LED since the button is not pressed
    digitalWrite(7, LOW);
  }
}
You may want to put a delay after writing to pin 7.
If the goal is to just turn on an LED when a button is pressed, don‘t use an Arduino as a simple circuit would suffice.